###### Robotics Update Controller Scheme
###### Transmission Bytes
Transmission bytes are the values that will be sent over the zigbee network. The values 0-255 can be sent. The range has been divided into smaller sections to allow for proper control of the robots. Each robot has been assigned a range of 30 values, the commands in these ranges will be similar and can be seen in a subsequent table. Eight ranges of 30 adds up to 240, this allows for fifteen global variables the all robots respond to. Two of these signals are a global start and stop, this would allow for complete control of the robots.

Decimal	Purpose
0	No Send
1-30	Robot 1 Definable Range
31-60	Robot 2 Definable Range
61-90	Robot 3 Definable Range
91-120	Robot 4 Definable Range
121-150	Robot 5 Definable Range
151-180	Robot 6 Definable Range
181-210	Robot 7 Definable Range
211-240	Robot 8 Definable Range
241	Global Unused
242	Global Unused
243	Global Unused
244	Global Unused
245	Global Unused
246	Global Unused
247	Global Unused
248	Global Unused
249	Global Unused
250	Global Unused
251	Global Unused
252	Global Unused
253	Global Unused
254	Global Stop Signal (Programmed, but unused)
255	Global Start Signal (Programmed, but unused)

###### Controller Buttons Mapping (w/ Corresponding Robot Definable Byte)
Each robot will see all values being sent out over the zigbee network, but will only respond to it’s corresponding commands. Each robot will be programmed using a different base value, this will tell the robot which range it responds to.
Button	Byte	Command
Left Stick 100%	Base	M1 - CW - 100
Left Stick 80%	Base + 1	M1 - CW - 80
Left Stick 60%	Base + 2	M1 - CW - 60
Left Stick 40%	Base + 3	M1 - CW - 40
Left Stick 20%	Base + 4	M1 - CW - 20
Left Stick -20%	Base + 5	M1 - CCW - 20
Left Stick -40%	Base + 6	M1 - CCW - 40
Left Stick -60%	Base + 7	M1 - CCW - 60
Left Stick -80%	Base + 8	M1 - CCW - 80
Left Stick -100%	Base + 9	M1 - CCW - 100
Right Stick 100%	Base + 10	M2 - CCW - 100
Right Stick 80%	Base + 11	M2 - CCW - 80
Right Stick 60%	Base + 12	M2 - CCW - 60
Right Stick 40%	Base + 13	M2 - CCW - 40
Right Stick 20%	Base + 14	M2 - CCW - 20
Right Stick -20%	Base + 15	M2 - CW - 20
Right Stick -40%	Base + 16	M2 - CW - 40
Right Stick -60%	Base + 17	M2 - CW - 60
Right Stick -80%	Base + 18	M2 CW - 80
Right Stick -100%	Base + 19	M2 - CW - 100
L1	Base + 20	Aux M1 - CW
L2	Base + 21	Aux M1 - CCW
R1	Base + 22	Aux M2 - C
R2	Base + 23	Aux M2 - CCW
X	Base + 24	Fire
	Base + 25
	Base + 26
	Base + 27
	Base + 28
	Base + 29
	Base + 30
Circle	-	Swap Directions
Square	-	Swap Sticks
Start	-	Reset to defaults
Up	-	Unused
Right	-	Unused
Down	-	Unused
Left	-	Unused
Triangle	-	Unused

###### Robot Base Bytes
Each robot/controller is assigned a base byte. From the base byte all commands are incremented from this value, this will ensure only the correct robot responds.

Robot	Base Byte
1	1
2	31
3	61
4	91
5	121
6	151
7	181
8	211

###### Controller Button w/ Software Component
As of right now the controller button output string is unknown. It will need to be tested.
Button	Software Component(s)